## Slide 1: Research Plan: Reliable Graph Reinforcement Learning for Transmission Grid Topology Control
Corentin Plumet
Master Thesis Proposal
Grid2Op + reliability-oriented evaluation
Underexplored direction: busbar-aware heterogeneous GRL
April 2026

## Slide 2: Why This Thesis Topic
Problem Statement
  Traditional optimization methods:
  Struggle with scalability
  Are too slow for real time decision making
  RL approaches:
  Remain mostly proof-of-concept on benchmark grids and simplified operating assumptions.
  The open question is not only whether GRL can act, but whether it acts reliably under nominal and stressed conditions.
Motivation
  Transmission operators need fast congestion management under renewable variability and unforeseen events.
  Topology actions are attractive because they can reroute flows before using costly redispatch.
  Reinforcement learning is appealing for sequential decisions, but the control space is huge and safety-critical.

## Slide 3: Short Literature Review
  Learning Methods
  Topology control is the main transmission-grid use case, with PPO, DQN variants, SMAAC, MCTS, and multi-agent methods.
  Graph encoders are increasingly used because the grid is naturally relational and topology changes alter the graph itself.
  Takeaway
  Structure in the controller matters at least as much as the RL algorithm choice.
  Hybrid Systems
  Recent surveys show that strong controllers are rarely pure end-to-end RL; they are hybrid systems.
  Dominant ingredients are action-space reduction, rule-based safety logic, simulator filtering, and imitation bootstrapping.

## Slide 4: Dive Into the Main Solutions Developped
One RL Agent with Safety Layers
  [7] uses a GCN with Double-Q / dueling RL and verifies top-Q actions with power-flow simulation.
  [1] trains PPO with dynamic action masking so infeasible busbar actions are never sampled.
  These methods keep one global controller but rely on hard engineering tricks to stay safe.
  Typical tricks are do-nothing fallback, pruning of symmetric actions, and simulator-based validation.
  Their weakness is sample efficiency: the agent still sees a huge discrete action space.
Planning and Model-based Methods
  [5] learns a GCN world model that predicts line loading for candidate topologies.
  MCTS expands a search tree over future actions and selects promising branches instead of brute-force exploration.
  Only states with acceptable predicted loading are kept, which prunes catastrophic branches early.
  [6] also uses MCTS, but combines it with double-dueling sub-agents on a reduced action space.
  This family trades extra planning cost for better action selection in a combinatorial control problem.

## Slide 5: Dive Into the Main Solutions Developped
Predict a target topology, not a raw switch
  [8] SMAAC and [3] predict a goal topology, then a low-level policy realizes it.
  Their key idea is the afterstate: learn from the resulting topology, not only from the raw switch action.
  That matters because different switching sequences can lead to the same effective substation configuration.
  First decide where to intervene, then decide how.
Multi-agent and Imitation-enhanced GRL
  [4] uses hierarchical multi-agent PPO/SAC where higher levels detect critical areas and lower levels act.
  [2] distributes control to line-level agents and shares a GAT encoder for local context.
  Multi-agent decomposition reduces the effective action space by assigning local responsibility to components.
  [2] and [9] use expert demonstrations or imitation learning to improve sample efficiency.
  The logic is practical: start from expert behavior, then let RL improve beyond it through interaction.

## Slide 6: Research Gap
  Limits of these studies
  No standardized Evalution: Evaluation protocols differ a lot across papers: rewards, seeds, horizons, contingencies, and grid sizes are inconsistent.
  Mostly Proof-of-Concept: Most studies rely on Grid2Op and relatively small IEEE-style benchmarks, with limited stressed-condition testing.
  Key ideas exist but not combined
  Imitation learning
  Advanced graph representation
  Safe RL

## Slide 7: Thesis Refinement
  Main Goal: Develop a hybrid GRL framework that improves
  Learning efficiency
  Robustness
  Safety
  For power grid topology control
  Research Questions:
  Do better graph representations improve performance ?
  Can imitation learning speed up training ?
  Do safety mechanisms improve stability ?
  How sensitive are results to evaluation setup ?
  For power grid topology control

## Slide 8: Approach
Proposed Approach
  Graph representation of grid
  Imitation learning (pretraining)
  Reinforcement learning (fine-tuning)
  Safety mechanism (action filtering)
  Combine strengths of all components
Methodology
System Design
  Graph Encoder: GNN heterogeneous
  Policy Model: PPO
Training Pipeline
  Stage 1: Imitation learning
  Stage 2: RL optimization
Safety Layer
  Action masking
  Feasibility checks

## Slide 9: Timeline
April - Baselines
  Set up Grid2Op pipeline
  Implement baseline
  Define metrics & run initial experiments
May – Graph Models
  Design heterogeneous graph representation
  Implement & compare GNN architectures
  Analyze impact vs baseline
June – Imitation Learning
  Generate expert data (heuristics)
  Train via behavioral cloning
  Evaluate pretraining performance
July – Reinforcement Learning
  Fine-tune with RL (PPO)
  Add safety mechanisms (action masking)
  Abalation studies
August – Evaluation
  Test on multiple scenarios & grids
  Evaluate generalization
  Compare with baselines

## Slide 10: References
[1] Batanero, E.A., Fernández, Á., Barbero, Á. Graph-enhanced model-free reinforcement learning agents for efficient power grid topological control (2025)
[2] Fabrizio, C., Losapio, G., Mussi, M., Metelli, A.M., Restelli, M. Power grid control with graph-based distributed reinforcement learning (2025)
[3] Qiu, Z., Zhao, Y., Shi, W., Su, F., Zhu, Z. Distribution Network Topology Control Using Attention Mechanism-Based Deep Reinforcement Learning (2022)
[4] Sar, E., Zocca, A., Bhulai, S. Multi-Agent Reinforcement Learning for Power Grid Topology Optimization (2023)
[5] Taha, S., Poland, J., Knezovic, K., Shchetinin, D. Learning to Run a Power Network under Varying Grid Topology (2022)
[6] Xu, P., Duan, J., Zhang, J., Pei, Y., Shi, D., Wang, Z., Dong, X., Sun, Y. Active Power Correction Strategies Based on Deep Reinforcement Learning—Part I: A Simulation-driven Solution for Robustness (2022)
[7] Xu, P., Pei, Y., Zheng, X., Zhang, J. A simulation-constraint graph reinforcement learning method for line flow control (2020)
[8] Yoon, D., Hong, S., Lee, B.J., Kim, K.E. Winning the L2RPN Challenge: Power Grid Management via Semi-Markov Afterstate Actor-Critic (2021)
[9] Zhao, Y., Liu, J., Liu, X., Yuan, K., Ren, K., Yang, M. A graph-based deep reinforcement learning framework for autonomous power dispatch on power systems with changing topologies (2022)